# The product line of rubber pressurizing strip microwave sirocco series vulcanization

>>> Introduction

"The product line of rubber pressurizing strip microwave sirocco series vulcanization" developed by Xinte Company of Beijing University of Chemical Technology can be used to manufacture the advanced rubber pressurizing strip of cars, planes, steamships, trains and the construction doors and windows. This product line adopts the special new cold feeding exhaust extrude machine, composite engine head and sirocco (or microwave--sirocco) series vulcanization. Through the using prove of many companies, not only the price is low (only 1/5～1/6 of the foreign machine), but also the production efficiency is very high, consume is low and the profits is high. The quality of pastern strip has reached the quality of the foreign pastern strip produced by the same product line, which is a new technology of low investment and high output.

At present, the development of auto is in flourish. The output has reached millions and there are more than 400 manufacturers. The auto has enter the families, whose demand for autos will be huge. The nationalization process of the auto become faster. The demand for the pressurizing strip will increase much more. So, manufacturing the pressurizing strip is a program which the investment is small, and the economic profits is very considerable.

The company can supply the complete equipments of the product line of rubber pressurizing strip microwave sirocco series vulcanization, and take charge of the following obligation:

1. According to the users' demand, supply all the equipments on time;

2. Take charge in training the specialists and workers of operating and maintaining the machine.

3. Take charge in the installation, debugging and after-sale service of all the equipments.

>>> Technology characteristics

1. This technology adopts the new cold feeding exhaust extrude machine, which can exhaust the volatile gas and moisture in the rubber and make the products possess the advantage of dense, good surface quality, reliable extruding stationary. So the senior rubber pressurizing strip can be produced;

2. Can supply the sirocco series vulcanization and microwave--sirocco series vulcanization equipments according to thedifferent demand of the rubber strip;

3. The degree of automata is high, only need 7 to 8 person to operate the whole product line;

4. Can change the products type conveniently through changing the type of the moulds;

5. The manufacturing speed can be adjusted between 1～20m / min.

>>>The Corp can supply the type of the "product line of rubber pressurizing strip microwave sirocco series vulcanization"

1. Single rubber "the product line rubber pressurizing strip microwave sirocco series vulcanization":

This product line is composed of the single screw cold feeding exhaust extrude machine and extrude engine head, which can produce kinds of single pastern pressurizing strip.

The product line equipments includes:

f90cold feeding exhaust extrude machine (one), f90 extrude engine head (one), sirocco series vulcanization box (three units), or microwave--sirocco vulcanization box (two units), cold traction equipment (one).

2. Three composed steel-core "product line rubber pressurizing strip microwave sirocco series vulcanization":

This line is composed of two cold feeding exhaust extrude machines and three composed engine head, can produces single pastern, double pastern, and steel-core pressurizing strip, which products reached several hundreds kinds.

The main equipments of this line includes:

f90 cold feeding exhaust extrude machine (one), f90 extrude engine head (one), sirocco series vulcanization box (three units) or microwave--sirocco vulcanization box (two units), cold traction equipment (one), core smash (one), core flex machine (one), stiletto (one), core storage shelf (one).

3. Four composed steel-core "product line rubber pressurizing strip microwave sirocco series vulcanization":

This product line is composed of three cold feeding exhaust extrude machines and four composed engine head, which can produce the single pastern, double pastern, double steel-core pastern strip, double steel-core pastern strip plastic composite, three steel-core pastern strip.

The main equipments of this line includes:

F75, f90 cold feeding exhaust extrude machine (each one), f50 feeding exhaust machine (one), four composite engine head (one), microwave vulcanization box (one units), sirocco series vulcanization box (two units), cold traction equipment (one), core smash (one), core flex machine (one), stiletto (one), core storage shelf (one).

>>>The contact of the program of "product line of rubber pressurizing strip microwave sirocco series vulcanization"

Contact: Liang Xiaoping

Tel: 010-64435043 64433048

Mobile Phone: 13801321949

Fax: 010-64435042

Add: Xinte Chemistry, Forth Floor of North Anhua Building, No.8, Yinghua West Street, Chaoyang District, Beijing

Code: 100029

Main technology parameter of cold feeding exhaust extrude machine Type Screw Diameter(mm) Screw Length(L/D) Screw Max-Revolution(r/min) Electric Machine Power(kw) Max-Productivity(kg/h) XJWP-45 φ45 16:1 5～70 11 35 XJWP-60 φ60 16:1 5～60 18.5 75 XJWP-65 φ65 16:1 5～60 22 80 XJWP-75 φ75 20:1 5～60 37 180 XJWP-85 φ85 20:1 5～60 45 200 XJWP-90 φ90 22:1 5～55 55 220 XJWP-115 φ115 18:1 5～55 75 400 XJWP-120 φ120 18:1 5～45 90 500

Main technology parameter of the normal cold feeding extrude machine Type Screw Diameter Screw Length Contrast Screw Max-Revolution Electric Machine Power Max-Productivity XJW-45 φ45 4.5:1 70 11 35 XJW-60 φ60 6:1 60 18.5 75 XJW-65 φ65 16:1 60 22 80 XJW-75 φ75 17:1 60 37 180 XJW-85 φ85 18:1 60 45 220 XJW-90 φ90 20:1 58 55 240 XJW-115 φ115 14:1 58 75 420 XJW-120 φ120 14:1 48 90 500

Main technology parameter of pin cold feeding extrude machine Type Screw Diameter Screw Length Contrast Screw Max-Revolution Electric Machine Power Max-Productivity XJD-60 φ60 10～12 80 17～22 120 XJD-65 φ65 10～12 80 25～30 150 XJD-90 φ90 12～14 60 40～55 360 XJD-120 φ120 12～16 55 75～100 780 XJD-150 φ150 12～16 45 150～185 1800 XJD-200 φ200 12～18 32 220～315 2600 XJD-250 φ250 12～20 26 355～500 3000